SECTION 203 – WATERING

203-1  DESCRIPTION

This item shall consist of applying City of Watford City furnished water required in the compaction of embankments, subgrades, subbases, base courses, and for other purposes in accordance with the requirements of these specifications or as directed by the ENGINEER.

203-2  CONSTRUCTION REQUIREMENTS

Water, when required, shall be applied at the locations, in the amounts, and during the hours, including nights, as approved by the ENGINEER.  An adequate water supply shall be provided by the City of Watford City.  The equipment furnished and used by the CONTRACTOR for watering shall be of ample capacity and of such design as to assure uniform application of water in the amounts directed by the ENGINEER.

The CONTRACTOR shall furnish all fittings, hoses, and equipment used in the loading of City furnished water.  If a water hydrant is used for furnishing water, the CONTRACTOR shall furnish a gate-type control valve, approved by the ENGINEER, to control water flow.  The hydrant valve shall be fully opened and under no circumstances will the hydrant valve be used for water flow control.  The CONTRACTOR shall apply for a hydrant meter supplied and installed by the City of Watford City Public Works Department and shall pay all installation and usage fees unless waived by the contract documents.

203-3  MEASUREMENT AND PAYMENT

203-3.1  Watering.  Watering shall be measured in the vehicle at the point of delivery by 1,000 gallon ("M" Gal.) units or by a meter supplied by the City of Watford City Public Works Department and paid for at the unit price bid for "Watering."